GOBOT http://gobot.io/
PWM https://github.com/sarfata/pi-blaster
CGO https://github.com/golang/go/wiki/cgo
cc2530dk http://www.ti.com/lit/ug/swru209b/swru209b.pdf

X11 Client Installation
To do this, install the xauth pachage, then simply install the applications you need, and apt-get will bring in other packages as needed to satisfy the dependencies.
sudo apt-get install xauth
X11 Server Installation
To install a minimal X11 on Ubuntu Server Edition enter the following:
sudo apt-get install xorg openbox

/*---------------------------------------------------------------------------*/
/* Setting parameter for ADCCON3

bit 7-6 :Selects reference voltage used for the sequence of conversions ----- เลือกแหล่งจ่ายในการอ้างอิงค่าสูงสุดของ analog input--
00: Internal reference ------อ้างอิงค่าจากภายในชิพ cc2530 มีค่า 1250mV (|= 0x0)
01: External reference on AIN7 pin ------อ้างอิงจากแหล่งจ่ายภายนอก (|= ADCCON3_EREF0)
10: AVDD5 pin :reference from v--------อ้างอิงจากไฟเลี้ยงชิพ <= 3.3V (|= ADCCON3_EREF1)
11: External reference on AIN6–AIN7 differential input------ไฟอ้างอิงสำหรับการเปรียบเทียบค่าความต่างของ Analog (|= ADCCON3_EREF1 | ADCCON3_EREF0)

bit5-4 :Sets the decimation rate for channels included in the sequence of conversions. The decimation
 rate also determines the resolution and time required to complete a conversion.
00: 64 decimation rate (7 bits ENOB) (|= 0x0)
01: 128 decimation rate (9 bits ENOB) (|= ADCCON3_EDIV0)
10: 256 decimation rate (10 bits ENOB) (|= ADCCON3_EDIV1)
11: 512 decimation rate (12 bits ENOB) (|= ADCCON3_EDIV1 | ADCCON3_EDIV0)

bit3-0 :Sequence channel select. Selects the end of the sequence. A sequence can either be from AIN0
 to AIN7 (SCH <= 7) or from the differential input AIN0–AIN1 to AIN6–AIN7 (8 <= SCH <= 11). For
 other settings, only one conversions is performed.
 When read, these bits indicate the channel number on which a conversion is ongoing.
0000: AIN0 (|= 0x0)
0001: AIN1 (|= ADCCON3_ECH0)
0010: AIN2 (|= ADCCON3_ECH1)
0011: AIN3 (|= ADCCON3_ECH1 | ADCCON3_ECH0)
0100: AIN4 (|= ADCCON3_ECH2)
0101: AIN5 (|= ADCCON3_ECH2 | ADCCON3_ECH0)
0110: AIN6 (|= ADCCON3_ECH2 | ADCCON3_ECH1)
0111: AIN7 (|= ADCCON3_ECH2 | ADCCON3_ECH1 | ADCCON3_ECH0)
1000: AIN0–AIN1 (|= ADCCON3_ECH3)
1001: AIN2–AIN3 (|= ADCCON3_ECH3 | ADCCON3_ECH0)
1010: AIN4–AIN5 (|= ADCCON3_ECH3 | ADCCON3_ECH1)
1011: AIN6–AIN7 (|= ADCCON3_ECH3 | ADCCON3_ECH1 | ADCCON3_ECH0)
1100: GND
1101: Reserved
1110: Temperature sensor (|= ADCCON3_ECH3 | ADCCON3_ECH2 | ADCCON3_ECH1)
1111: VDD/3
>>>>>>AIN0 - AIN7 = P0_0 - P0_7 <<<<<<
Aref : pin external voltage applied to the AIN7.Or a differential
voltage applied to the AIN6–AIN7 inputs

Analog external referennce	->TineConvertion = (decimation rate + 16) x 0.25 microsec.
ADC sampling frequency of 4 MHz is generated by fixed internal division.

// ADCCON3
#define ADCCON3_EREF1 0x80
#define ADCCON3_EREF0 0x40
#define ADCCON3_EDIV1 0x20
#define ADCCON3_EDIV0 0x10
#define ADCCON3_ECH3 0x08
#define ADCCON3_ECH2 0x04
#define ADCCON3_ECH1 0x02
#define ADCCON3_ECH0 0x01

*/